Single Disks

(a) Side view of a magnetic disk. (b) Top view of a magnetic disk

Computing Disk Service Time

Architecture of a typical I/O subsystem

Nomenclatura

Computing Disk Service Time

Computing Disk Service Time

Types of workload

Computing Disk Service Time

Computing Disk Service Time

Disk service times equations

Esempio DB Server

Arrival rate: 20 req/sec

Tipo di workload:

20% random

80% sequenziale

Block size: 2,048 bytes

Disk Revolution Time: 7,200 RPM

Seek Time: 9 msec

Transfer Rate: 20 MB/sec

Controller Time: 0.1 msec

( Latency = ½ x 60/7,200 x 1,000 = 4.17 msec

( TransferTime = 2,048/(106 x 20) x 1,000 = 0.1 msec

( Average Service Time (Random Request) = 0.1+ 9 +4.17 + 0.1 =13.4 msec

Ud = ArrivalRate x (RandomSeek + AverageLatency + AverageTransferTime)

( Ud = 0.020 x (9+4.17+0.1) = 0.27

( Pmiss = 1/24 = 4.2 %

( AverageSeekTime = 9/24 = 0.38 msec

( AverageRotationalLatency =

½+23(1+0.27)/2  x 60x1,000 = 5.25 msec

- 7,200

( Average Service Time (Sequential Request) = 0.1+ 0.38 +5.25 + 0.042x0.1 =5.73 msec

( Average Service Time = 7.25 msec

Disk Arrays

Disk array

Nomenclatura

- nr : number of stripe units reads by a read request

- nw : number of stripe units modified by a write request

- (rarray: arrival rate of read requests to the disk array

- (warray: arrival rate of write requests to the disk array

- (rdisk: arrival rate of read requests to any of the disk in the array

- (wdisk: arrival rate of write requests to any of the disk in the array

- N: number of physical disks in the array

- Srarray: average service time at a disk array for read

- Swarray: average service time at a disk array for read

  - Number of possible groups of nr disks:

  - Each disk in the array belongs to

groups of nr disks.

  - Fraction of read requests to the array that goes to any of the disks (uniform distribution to all disks)

  - Arrival rate of disk requests at a disk

  - Arrival rate of write requests to any disk in the array

( Average service time of read request at disk array

where Rrdisk i is the average response time of read requests at disk i.

( Average service time of write request at disk array

where Rwdisk i is the average response time of write requests at disk i.