## Slide 1: Improving Sequential Simulation Based Methods for Dense Sensor SLAM
  Giorgio Grisetti
  grisetti@dis.uniroma1.it

## Slide 2: Mapping?
A mobile robot should be able to navigate.
The position can be know up to the map knowledge.
Some tasks make it impossible to know the map (e.g. exploration).
Acquiring the map is essential for moving towards fully autonomous robots.

## Slide 3: But..
For building a map the robot requires to be aware of its position.
Errors in the pose affects in the map, and vice-versa.
The map and the pose should be concurrently evaluated.
SLAM=Simultaneous Localization and Mapping

## Slide 4: Goals of this talk
Provide an overview of the SLAM techniques.
Introduce the Bayesian approach to SLAM.
Introduce Rao-Blackwellized particle filters.
Give an overview of a state of the art SLAM approach.

## Slide 5: Key Issues in SLAM
Mapping? What does it mean?
How to represent a map.
Which algorithm to choose.
The Loop Problem.

## Slide 6: Mapping
A robot moves in an unknown environment,
and acquires data.
Data comes as noisy measurements:
We want to determine:
relative movements
environment
trajectory
map
Which best explains that measurements.

## Slide 7: Probabilistic Mapping
Find the map and a robot trajectory that maximizes the likelihood of a set of sensor readings.
Local minima Greedy search impossible
Track a posterior over maps and trajectories:

## Slide 8: Map Representations
Dense Maps
  Easy to implement and update
  Rich of information
  Loses inter-cell relations
  Spatially complex
Landmark Maps
  Compact
  Allow to represent a full posterior
  Drop a lot of information

## Slide 9: Representations and Estimation
 | Dense | Landmark
Kalman Filter | No | Ok
Particle Filter | Ok | Ok
Maximum Likelihood | Ok | -
Global ML | Indirect | Ok
Expectation Maximization | Indirect | Ok

## Slide 10: The Loop Problem
Correct loop detection Uncertainty reduction
  Loop: part of the robot trajectory in which the first and the last sight are overlapping.

## Slide 11: On Line Estimation
Within the on-line techniques Bayes Filters are the most used tools in SLAM
 | close loop | revise past | multi hp
Kalman Filter | Yes | Yes | No
Particle Filter | Yes | No | Yes
Max Likelihood | No | No | No

## Slide 12: Bayes Filtering
Define SLAM as a state estimation problem:
Determine
given

## Slide 13: Bayes Filtering and Mapping
The state space of the dynamic system is the cross product among maps and robot poses.
We want to estimate:
pose
map

## Slide 14: Markov Assumption
If the Markov assumption holds we can recursively estimate the state as:
prior
likelihood
transition model

## Slide 15: Bayes Filters
Making different assumptions on the observed system, and the noise model leads to different filtering algorithms.
 | system | PDF
KF EKF UKF | linear linearized 2nd order | normal
PF | any | sampled

## Slide 16: Kalman Filters and SLAM
Tracks a linearized system.
State space is the landmark and robot pose state.
Fully correlated posterior represented with mean and covariance matrix
Analytical update
Posterior not always normal
World not made by landmarks
Landmark identification can fail
Filter Failure
but

## Slide 17: Particle Filters and SLAM
Tracks an arbitrary system. State space is the robot pose.
Allows to use dense maps.
Posterior represented as trajectories and conditional maps.
Numerical pose update, analytical map update.
Multi Hypotheses.
Not clear how many samples are required.
Unable to revise the past.
but

## Slide 18: Particle Filter Issues
PDF represented in sampled form
Ideally one would draw samples from:
Impossible since a closed form is generally unknown

## Slide 19: Importance Sampling Principle
If we know a function
, possibly similar to ,
sampling from
and evaluating
pointwise,
leads to:
where

## Slide 20: Sequential Estimation
A key problem is to carry on the estimate without changing the past generated trajectories.
This is possible if choosing a of a particular form.
Particluar cases are:
The transition model
The informed transition model

## Slide 21: Particle Filter Algorithm
Estimate the samples for the next generation:
Evaluate the importance weights, according to I.S.
Suppress degeneracy by resampling

## Slide 22: Key Issues in Particle Filters
How to choose the Importance Function?
When to perform resampling?
Does it exist a quality measure for the estimate?
In general the I.F. is system dependent. The I.F. tuning strongly influences the P.F. behavior.
Resampling can kill good trajectories.
In a good approximation the sample weights should be equal.

## Slide 23: RBPF Particle Filters and SLAM
Relies on the following factorization:
Estimate independently the trajectories,
and the maps conditioned to the trajectories
Using a sampled representation of the trajectories,
and update analytically the maps
trajectory sample
weighting factor
conditional map

## Slide 24: RBPF Particle Filters
Draw the next pose sample from an I.F.
Evaluate the weight according to I.S.
Resample
Update the map

## Slide 25: FastSLAM
Landmark based map.
Particle Filter for robot trajectories.
Conditional Kalman Filter for Landmarks.
Transition Model chosen as IF.

## Slide 26: Grid FastSLAM
A map for each pose sample
Uses the odometry model as transition function
Odometry improved through scan-matching
Likelihood peaked w.r.t. transition model

## Slide 27: FastSLAM weakness
Using the odometry as I.F. and an accurate sensor requires an high number of samples.
Most of the samples are wasted in the weighting phase
The number of particles required for convergence in principle grows exponentially with the path size.
Resampling can kill the good map.
Generate samples only when needed
Perform active resampling

## Slide 28: Improving GridFastSLAM
Sample from an informed transition model.
Not available in closed form
Perform resampling only when the quality of the approximation gets worse.
How to decide when to resample?
?

## Slide 29: Improved Proposal Distribution
accurate Sensor
peaked pikelihood
peaked informed I.F.
local gaussian approximation
can sample form a
peaked I.F.
considering z reduces the proactiveness
decrease
sample #
good performance
without resampling

## Slide 30: Computing the likelihood
The likelihood is peaked w.r.t
transition model.
Can consider it constant

## Slide 31: Estimating the closed from

## Slide 32: The importance weights
Importance Samping principle still holds:

## Slide 33: Resampling
Use a quality factor for the particle approximation:
In the ideal case the weights would be equal.
An indirect measure of the weights variance.
Resample when it drops below a given threshold.

## Slide 34: Overall Algorithm
For all particles
  Incorporate the odometry.
  Compute the local maxima of the scan matcher,
  given the particle map.
  Compute the likelihood statistics, and draw a new sample.
For all particles
  Compute the weights
If Neff>threshold
  Resample
For all particles
  Compute the new map given the reading

## Slide 35: Effects of the imporved proposal
An environment dependent particle dispersion w/o resampling.
An order of magnitude less particles needed.

## Slide 36: Neff Behavior
Slow decay in the unknown
Fast Drop in
loop closure
Constant in the known

## Slide 37: MIT Killian Court
1.9 km
200 particles
2h acquisition time
3h processing time

## Slide 38: Freiburg Campus
1.7 km
30 particles
1h acquisition time
30’ processing time

## Slide 39: Conclusions
An order of magnitude less particles than similar approaches.
On line maps of big environments.
Many experiments on third party logs confirmed the validity of the approach.
(www.informatik.uni-freiburg.de/~stachnis)

## Slide 40: Future Works
Exploit the loop/non-loop situation for increasing the efficiency
Estimate the past trajectories with smoothing
The mapper goal:
Constant update, linear loop closure